# Published as: Brennan, R.B., Fenton, O., Rodgers, M., Healy, M.G. 2011. Evaluation of chemical amendments to control phosphorus losses from dairy slurry. Soil Use and Management 27(2): 238-246. doi: 10.1111/j.1475-2743.2011.00326.x

Evaluation of chemical amendments to control phosphorus losses from dairy slurry.

# R.B. Brennan1, O. Fenton2, M. Rodgers1, M.G. Healy 1*

1Department of Civil Engineering, National University of Ireland, Galway, Co. Galway, Rep. of Ireland.

2Teagasc, Johnstown Castle, Environmental Research Centre, Co Wexford, Rep. of Ireland

# Corresponding author. Tel: +353 91 495364; fax: +353 91 494507. E-mail address: mark.healy@nuigalway.ie

# RUNNING HEAD TITLE:

# Chemical amendments to control phosphorus

# Abstract

The aim of this paper is to identify chemicals with the potential to reduce P losses from agricultural grassland arising from the land application of dairy cattle slurry. It also aims to identify optimal application rates and to estimate associated costs. The cost of chemical amendments was estimated based on cost of chemical, chemical delivery, addition of chemical to slurry, volume increases during slurry agitation, and slurry spreading costs. First, batch tests were carried out to identify appropriate chemical and phosphorus sorbing materials (PSMs) to be considered as potential amendments to control P in runoff from dairy cattle slurry. Then, the best seven treatments were examined in a novel agitator test. Optimum application rates were selected based on percentage removal of dissolved reactive phosphorus (DRP) in overlying water and the estimated cost of amendment. At optimum application rates, alum reduced the DRP in overlying water by 94%, aluminium chloride (AlCl2) by 92%, ferric chloride (FeCl2) by 88%, lime by 81%, aluminium water treatment residuals (Al-WTR; sieved to <2mm) by 77%, Al-WTR sludge by 71%, flyash by 72%, and flue gas desulphurisation by-product by 72%. Alum was the most cost-effective chemical amendment, and was capable of greater than 90% reduction in soluble P in overlying water. The optimum FeCl2 amendment was less expensive, but not quiet as effective. AlCl2 and lime are expensive, and despite the attractiveness of using PSM, those examined were not cost effective at P reductions of greater than 85%.

Keywords: Water treatment residual; alum; aluminium chloride; ferric chloride; lime; flue gas desulphurisation by-product; flyash.

# Introduction

Repeated application of organic and mineral fertilizer causes soil test phosphorus (STP) to build up in the soil and, during rainfall events, may cause nutrients to be released to surface runoff (Hao et al., 2008). Runoff from grassland pastures and meadow fields following slurry application can result in incidental phosphorus (P) losses and has the potential to transport nutrients to surface water (Smith et al., 2001a). This may result in eutrophication of rivers and fresh water lakes.

Chemical amendments can either be added directly to the manure before land application (Moore et al., 1998), spread on the ground before manure application (McFarland et al., 2003), or incorporated into the ground (Novak and Watts, 2005).

Aluminium (Al) compounds are the preferred amendment, as calcium phosphate minerals are not as stable (Moore et al., 1998), and ferrous compounds can break down in acidic soil conditions (Smith et al., 2001b). To date, work involving alum addition to dairy cattle slurry has been largely limited to laboratory batch studies.

Novak and Watts (2005) incorporated aluminum water treatment residuals (Al-WTR) into the upper 15 cm of topsoil at a 1-6% soil volume. This lowered water extractable P (WEP) in the soil by between 45% and 91% after an 84-d incubation period.

Coal combustion by-products have potential to mitigate P loss from soil following manure application (Dao, 1999). Stout et al. (1998) reported that by blending flyash with soil at 0.01 kg/kg soil, Mehlich-III P (M3-P) and WEP were lowered by 13% and 71%, respectively. Flue gas desulphurisation (FGD) by-product, applied at 0.01 kg/kg soil, lowered M3-P by 8% and WEP by 48%.

McGrath et al. (2010) examined the sorption and retention mechanisms of several PSMs and found the degree of sorption to be strongly influenced by the solution pH, buffer capacity, and ionic strength of amendments.

Present agricultural practice is governed by The European Communities (Good Agricultural Practice for Protection of Waters) Regulations 2009 (S.I. No. 101 of 2009), drafted to comply with the Nitrates Directive (91/676/EEC; EEC, 1991). The Water Framework Directive (WFD; 2000/60/EC, OJEC, 2000) recommends research and development of new pollution mitigation measures to achieve the 2015 target of surface and groundwaters of ‘good status’. Therefore, there is potential that chemical treatment of dairy cattle slurry maybe used to control P in Ireland.

The ‘agitator test’ is a simple and effective test that has been be used to investigate the release of P from soil (Mulqueen et al., 2004). This test was chosen to evaluate the effectiveness of the chemical amendments in reducing incidental soluble P loss from slurry as it is more realistic than traditional batch-type experiments.

The objectives of this study were to use the agitator test: (i) to determine if there is potential use of chemical amendments to reduce P loss from the soil surface after land application of dairy cattle slurry; (ii) to identify optimum amendment application rates; (iii) to evaluate the feasibility of these treatments, and to estimate the cost of each treatment.

# Materials and Methods

# Soil preparation and analysis

The soil samples used in this study were taken from a local dry stock, extensively operated farm with undulating terrain. 120-mm-high, 100-mm-diameter aluminium coring rings were used to collect the samples. The grass was left intact and all soil cores were stored at 11°C in a cold room prior to testing. All agitator tests were carried out within 21 d of sample collection and tests were conducted in triplicate (n=3).

Soil samples – taken from the same location - were air dried at 40 °C for 72 hr, crushed to pass a 2 mm sieve, and analysed for P using MP-3 extracting solution (Mehlich, 1984) and Morgan’s P using Morgan’s extracting solution (Bourke et al., 2007). Soil pH was measured in triplicate after Bourke et al. (2007). Shoemacher-McLean-Pratt (SMP) buffer pH was determined and the lime requirement (LR) of the soil was calculated after Pratt and Blair (1963). Particle size distribution (PSD) was determined using B.S.1377-2:1990 (BSI, 1990a). Organic content of the soil was determined using the loss of ignition (LOI) test (B.S.1377-3; BSI, 1990b).

# Slurry sampling and analysis

Dairy cattle slurry from replacement heifers was used in this study. The slurry tanks were agitated until the slurry was homogenized, and slurry samples were collected in 10-L drums and transported to the laboratory. Slurry samples were stored at 4°C until immediately prior to the start of the agitator test. Slurry pH was determined using a pH probe (WTW, Germany) at 0 hr and 24 hr. The WEP of slurry was measured after 24 hr after Kleinman et al. (2007). The total phosphorus (TP) of the dairy cattle slurry was determined after Byrne (1979). Potassium (K) and magnesium (Mg) were analyzed using an On varian Spectra 400 Atomic Absorption instrument, and analyses for nitrogen (N) and P were carried out colorimetrically using an automatic flow-through unit.

# Analyses of PSMs

# The pH of the PSMs was measured in triplicate using 2:1 deionised water: dry amendment ratio after Bourke et al. (2007). In the case of the Al-WTR sludge, it was possible to measure pH of the sludge with a pH probe. Dry matter (DM) content was determined by drying at 40°C for 72 hr. Total metal and P of the PSMs was measured by ‘aqua regia’ digestion using a Gerhard Block digestion system (Cottenie & Kiekens, 1984), which is described by Fenton et al. (2009). WEP of the PSMs was determined after Dayton and Basta (2001).

# Slurry treatment

Tests were carried out to determine the effectiveness of various chemical amendments to treat the dairy cattle slurry. The best seven  P-sorbing amendments were examined in the agitator test; these were: industrial grade alum (8% Al2O3, Al2(SO4)3.nH2O); laboratory grade aluminium chloride (AlCl3.6H2O); FeCl2; burnt lime (Ca(OH)2); Al-WTR, sieved to less than 2 mm (Al-WTR-1); Al-WTR homogenised sludge (Al-WTR-2); flyash; and FGD (Table 1). Chemical amendments were applied based on Al:TP stoichiometric rate, and PSMs were applied based on a kg/kg  weight basis (slurry dry matter). The Al-WTR was obtained from a local water treatment plant (WTP) and the coal combustion by-products were provided by the Electricity Supply Board (ESB) at Moneypoint, Co. Clare.

The pH of the amended slurry was measured prior to application at t=0 hr. Samples were taken to determine DM and WEP of the amended slurry (after Kleinman et al., 2007). Slurry and amended slurry were applied to surface of the grassed soil at a rate equivalent to 40 kg TP/ha (50 m3 slurry/ha). For each treatment, slurry samples (n=3) with the same volume as applied to the grass sample in the agitator test were spread at the bottom of a beaker to allow pH and WEP to be measured at 24 hr without disturbing the sample used in the agitator test.

# Agitator test

Prior to the start of the agitator test, the intact soil samples were transferred into the beakers. The depth of soil in the beakers ranged from 40 mm to 50 mm; this was considered sufficient to include the full depth of influence (Mulqueen et al., 2004).

The agitator test comprised 10 different treatments: a grassed sod-only treatment (the study control); grassed sod receiving dairy cattle slurry at a rate equivalent to 40 kg TP/ha, and grassed soil receiving 8 different chemically treated slurries (Table 1) applied at a rate equivalent to 40 kg TP/ha. Each of the 8 amendments were applied at 3 different rates (high, medium and low) in triplicate (n=3). The chemically amended slurry was initially applied to the soil (t=0 hr), and was then allowed to interact for 24 hr prior to saturation of the sample. After 24 hr (t=24 hr), samples were saturated by gently adding deionised water to the soil sample at intermittent time intervals until water pooled on the surface. The sample was saturated for 24 hr (t=48 hr). Immediately after saturation was complete, 500 ml of deionised water was added to the beaker. The agitator paddle was then lowered to mid-depth in the overlying water and rotated at 20 rpm for 24 hr.

# Water sampling and analysis

Water samples (4 ml) were taken at 0.25, 0.5, 1, 2, 4, 8, 12 and 24 hr after the start of the test. All samples were filtered immediately after sample collection using 0.45 μm filters and placed in a freezer (after APHA, 1995) prior to being analysed colorimetrically for DRP using a nutrient analyser (Konelab 20, Thermo Clinical Labsystems, Finland). The DRP concentrations were used to calculate the mass of DRP in the water overlying the soil samples in the beaker, taking into account the water volume reduction as the test progressed. All water samples were tested in accordance with standard methods (APHA, 1995).

# Statistical Analysis

# The results were analysed using SAS (SAS Institute, 2004). Proc Mixed was used to model the factorial structures (amendment x application rate; and amendment x application rate x time) in the experiment in order to allow for heterogeneous variance across treatments.  A group variable was fitted to allow comparisons between the control treatments and the factorial combinations. A multiple comparisons procedure (Tukey) was used to compare means.

# Results and Discussion

# Soil analysis results

The soil used in this study had a M3-P concentration of 107±2.8 mg P/kg, Morgan’s P concentration of 12.3±0.49 mg/L and a soil pH of 5.6 ±0.1. The SMP buffer pH of the soil was 6.1±0.2 and the LR was calculated to be 9.9 ±1 t/ha. The soil used in this study comprised 15% gravel, 72% sand, and 13% fines, and had an organic matter content of 16.2±0.2%.

# Slurry and by-product analyses

Slurry used had TN of 3982±274 mg/L, TP of 803±37 mg/L, TK of 4009±482 and pH of 7.3±0.1. Slurry WEP values at 24 hr are tabulated in Table 1.

Table 2 shows the properties of the PSMs used in this study, the load of metals per hectare for optimum treatment, the maximum permissible annual average rates of addition of certain heavy metals to mineral and organic soils over a 10-yr period, and the limits on metal concentrations for potable water abstraction.

In a 20-yr plot study, Moore and Edwards (2005) found that after 10 yr, exchangeable Al was lower in plots fertilized with untreated litter and alum-treated litter than in plots receiving NH4NO3. Soil pH, and not the total Al content, controls Al availability. Therefore, repeated alum treatment will not lead to an increase in Al availability.

# Effectiveness of chemical amendments and PSMs in reducing DRP in overlying water.

The overall statistical analysis showed that there was a significant interaction between treatment and application rate, but that the interaction effects were small compared to the main effects. Comparisons of means were made from the interaction table. Figure 1 shows the mass of DRP in the water overlying the untreated soil and slurry-only treatments in the agitator tests. The reductions in mass of DRP in the overlying water for each amendment at 3 rates are tabulated in Table 1. Effervescence did not occur at the lower application rates. However, slurry volume increased by approximately 50% when alum was applied at 2.44 Al:TP. Lefcourt and Meisinger (2001) reported similar results, recommending that alum be added slowly. The addition of AlCl3 increased the difficulty of handling the slurry compared to the alum treatment, due to formation of foam on the surface of the slurry. This phenomenon was also noted by Smith et al. (2001b). FeCl2 was very effective and these results were in agreement with Moore and Miller (1994). However, it was not as efficient as alum or AlCl3 treatments.  Lime was less effective than Fe and Al-based compounds.

In this study, Al-WTR-1 reduced soluble P in water overlying the soil by 31%, 77% and 74% when applied at rates of 0.28, 0.69, and 1.4 kg of dry matter of sludge/kg of dry matter of dairy cattle slurry, respectively (0.28 kg/kg versus 1.4 kg/kg rates, p=0.003, no significant difference between the 0.69 kg/kg and 1.4 kg/kg rates). Homogenised Al-WTR-2 reduced soluble P in water overlying the soil by 0%, 71% and 67%, when applied on an equivalent basis. While not statistically significant, the irregularity between the 0.69 and 1.4 kg/kg treatment rates was found to be consistent across sieved and sludge treatments. McGrath et al. (2010) observed a 91% reduction in soluble P at when Al-WTR was applied at 0.2 kg/kg. The WTR used by McGrath et al. (2010) had Fe of 3.1% and Al of 7.6% - higher than the composition of WTR used in this study.

Flyash and FGD reduced soluble P in cattle slurry by 72% (versus control, p<0.0001) and 89% (versus control, p<0.0001), respectively, when applied at 4.2 kg/kg and 5.6 kg/kg, respectively. These rates of addition are higher than those used in previous studies (Dao, 1999; Dou et al., 2003).

Statistical analysis found that there was evidence of a three-way interaction between amendment, rate of application and time, but that the interaction was on a smaller scale than the main effects of amendment and time. Initially, the pH of the slurry was 7.3 ±0.5 (p<0.0001); the acidifying additives increase acidity of the slurry. Meisinger et al. (2001) found that pH would need to be lower than 5 to significantly reduce gaseous emissions. Lime addition increased the pH to a maximum value of 8.8 (p<0.0001). Application of Al-WTR, flyash and FGD did not significantly alter slurry pH initially.

At t=24hr, slurry pH increased to 7.8 (p<0.0001), while the effects of the acidifying additives reduced. Lime-treated slurry pH increased to 10.3 (p<0.0001). The pH of Al-WTR, flyash and FGD treatments also increased. Flyash had a pH of 9.3 (p<0.0001) at the optimum application rate. The pH of the overlying water was not measured.

McGrath et al. (2010) demonstrated that Ca and Mg-rich PSMs were most effective at P precipitation when manures or solution have sufficient buffering capacity to maintain a pH of between 6.5 and 7.5, and that Fe and Al-based compounds were more effective at low pH. This was consistent with the study findings.

Cost analysis of all treatments

The cost of each treatment per cubic metre of slurry and for a 100-livestock unit farm is shown in Table 1. The cost of chemical amendment was calculated based on the estimated cost of chemical, chemical delivery, addition of chemical to slurry, increases in slurry agitation, and slurry spreading costs as a result of increased volume of slurry as a consequence of adding amendments.

Figure 2 shows the total cost of chemical amendment of dairy cattle slurry, including spreading and agitation costs, plotted against the potential reduction in DRP lost to overlying water and the percentage reduction in DRP release to overlying water.

Conclusions

The findings of this study are:

(1) Alum is the most cost-effective chemical amendment capable of greater than 90% reduction in soluble P in overlying water at an additional cost of €4.40/m3 slurry;

(2) FeCl2 is the second most cost-effective chemical amendment with an 88% reduction in soluble P in overlying water at an additional cost of €3.60/m3 slurry;

(3) AlCl3 (€6.40/m3) and lime (€5.90/m3 slurry additional cost) applied at rates used in this study, are expensive compared to alum and FeCl2 and alum;

(4) Ca-based compounds (Ca(OH)2 and FGD) are much less effective at removing P than Fe and Ca compounds. This due to the inability of slurry to buffer the pH of slurry sufficiently to optimise Ca-P bond formation;

(5) Flyash results in a 72% reduction in DRP in the overlying water (€5.90/m3 slurry additional cost).

(6) Alum-based drinking water treatment residuals reduce the loss of soluble P from dairy cattle slurry by 71% at €1.20/m3 slurry additional cost, provided that the farmer has additional storage facilities. In addition, Al and Fe-rich WTRs may be more effective at lower application rates.

(7) Further work is necessary to prove that there is no risk to water quality associated with these treatments.

# Acknowledgments

# The first author gratefully acknowledges the award of a Walsh Fellowship by Teagasc to support this study. The authors are also very grateful for assistance provided by Teagasc and NUI Galway technicians, with special mention to Con Dowdall and Peter Fathy. They also wish to thank Patricia McGrath, who provided the soil samples, and to Cecile Labonne, who was a great help during the study.

# References

American Public Health Association (APHA). 1995. Standard methods for the examination of water and wastewater. APHA, Washington.

Bourke, D., Hochstrasser, T., Nolan, S. & Schulte, R. 2007. Historical grassland turboveg database project: 2067 relevés recorded by Dr. Austin O’Sullivan 1962 – 1982. Final report. Teagasc, Johnstown Castle, Co. Wexford, Ireland. Available at: www.teagasc.ie/research/reports/environment/5653/eopr-5653.pdf.; accessed 6/1/10.

British Standards Institution. 1990a. British standard methods of test for soils for civil engineering purposes. Determination of particle size distribution. BS 1377:1990:2. BSI, London.

British Standards Institution. 1990b. Determination by mass-loss on ignition. British standard methods of test for soils for civil engineering purposes. Chemical and electro-chemical tests. BS 1377:1990:3. BSI, London.

Byrne, E. 1979. Chemical analysis of agricultural materials – methods used at Johnstown Castle Research Centre, Wexford. Published by An Foras Taluntais.

Cottenie, A. and L. Kiekens. 1984. Report of results of the inter-laboratory comparison: Determination of the mobility of heavy metals in soils. In P. L’Hermite and H.D. Ott (ed.) Processing and use of sewage sludge. Reidel, Dordrecht, The Netherlands.

Dao, T.H. 1999. Co-amendments to modify phosphorus extractability and nitrogen/phosphorus ratio in feedlot manure and composted manure. Journal of Environmental Quality 28, 1114-1121.

Dayton, E.A. and Basta, N.T. Characterisation of drinking water treatment residuals for use as a soil substitute. Water Environment Research, Vol. 73, No. 1 52-57. Available at: http://www.jstor.org/stable/25045460; accessed 22/1/10.

Dou, Z., Zhang, G.Y., Stout, W.L., Toth, J.D. & Ferguson, J.D. 2003. Efficacy of alum and coal combustion by-products in stabilizing manure phosphorus. Journal of Environmental Quality 32, 1490-1497.

EEC. 1991. Council Directive concerning the protection of waters against pollution caused by nitrates from agricultural sources. Council of the European Communities, 91/676/EEC.

Official Journal of the European Communities, 2000. Directive 2000/60/EC of the European Parliament and of the council of 23 October 2000 establishing a framework for Community action in the field of water policy. 72p.

Fay, D. Kramers, G. Zhang, C.   "Soil Geochemical Atlas of Ireland". Associated datasets and digitial information objects connected to this resource are available at: Secure Archive For Environmental Research Data (SAFER) managed by Environmental Protection Agency Ireland. Available at: http://erc.epa.ie/safer/resource?id=4856ff8c-4b2b-102c-b381-901ddd016b14; accessed 12/1/10.

Fenton, O., M.G. Healy, and M. Rodgers. 2009. Use of ochre from an abandoned acid mine in the SE of Ireland for phosphorus sequestration from dairy dirty water. Journal of Environmental Quality 38, 1120 – 1125.

Hao, X., Godlinski, F. & Chang, C. 2008. Distribution of phosphorus forms in soil following long-term continuous and discontinuous cattle manure applications. Soil Science Society of America Journal 7, 90-97.

Kleinman, P.J.A., Sullivan, D., Wolf, A., Brandt, R., Dou, Z., Elliott, H., Kovar, J.,  Leytem, A., Maguire, R.,  Moore, P., Saporito, L., Sharpley, A.N., Shober, A., Sims, T., Toth, J., Toor, G., Zhang, H. & Zhang, T. 2007. Selection of a water extractable phosphorus test for manures and biosolids as an indicator of runoff loss potential. Journal of Environmental Quality 36, 1357-1367.

Lefcourt, A.M. & Meisinger, J.J. 2001. Effect of adding alum or zeolite to dairy slurry on ammonia volatilisation and chemical composition. Journal of Dairy Science 84, 1814-1821.

McFarland, A.M.S, Hauck, L.M. & Kruzic, A.P. 2003. Phosphorus reductions in runoff and soils from land-applied dairy effluent using chemical amendments. Texas Journal of Agriculture and Natural Research 16, 47-59.

McGrath, J.M., C.J. Penn, R.B. Bryant, and M.A. Callahan.  2010.  Use of industrial byproducts to sorb and retain phosphorus in animal manure.  In progress.

Mehlich, A. 1984. Mehlich 3 soil test extractant: A modification of the Mehlich 2 extractant. Communications in Soil Science and Plant Analysis 15, 1409-1416.

Meisinger, J.J., Lefcourt, A.M., Van Kessel, J.A. &Wilkerson, V. 2001. Managing ammonia emissions from dairy cows by amending slurry with alum or zeolite or by diet modification. Proceedings of the 2nd International Nitrogen Conference on Science and Policy. The ScientificWorld 1(S2), 860-865.

Moore, P.A. Jr. & Miller, D.M. 1994. Decreasing phosphorus solubility in poultry litter with aluminium, calcium and iron amendments. Journal of Environmental Quality 23, 325-330.

Moore, P.A. Jr., Jaynes, W.F. & Miller, D.M. 1998. Effect of pH on the solubility of phosphate minerals, in: Blake, J.P., Patterson, P.H. (Eds.) Proc. 1998 Natl. Poultry Waste Manage. Symp., Springdale, AR.19-21 Oct. 1998. Auburn Univ. Print. Serv., Auburn, AL, pp. 328-333.

Moore, P.A. Jr. & Edwards, D.R. 2005. Long-term effects of poultry litter, alum-treated litter and ammonium nitrate on aluminium availability in soils. Journal of Environmental Quality 34, 2104-2111.

Mulqueen, J., Rodgers, M. & Scally, P. 2004. Phosphorus transfer from soil to surface waters. Agricultural Water Management 68, 91-105.

Novak, J.M. & Watts, D.W. 2005. An alum-based water treatment residual can reduce extractable phosphorus concentrations in three phosphorus-enriched coastal plain soils. Journal of Environmental Quality 34, 1820-1827.

Pratt, P.F. & Blair, F.L. 1963. Buffer method for estimating lime and sulphur applications for pH control of soils. Soil Science 93, 329.

SAS (2004). SAS/STAT® User’s Guide. Cary, NC: SAS Institute Inc.

S.I.101.2009. European Communities (Good Agricultural Practice for Protection of Waters) Regulations 2009. Available at:

http://www.environ.ie/en/Legislation/Environment/Water/FileDownLoad,19875,en.pdf; accessed 12/1/10.

Smith, K.A., Jackson, D.R. & Withers, P.J.A. 2001a. Nutrient losses by surface run-off following the application of organic manures to arable land. 2. Phosphorus. Environmental Pollution 112, 53-60.

Smith, D.R., Moore, P.A., Griffiths, C.L., Daniel, T.C., Edwards, D.R. & Boothe, D.L. 2001b. Effects of alum and aluminium chloride on phosphorus runoff from swine manure. Journal of Environmental Quality 30, 992-998.

Stout, W.L., Sharpley, A.N. & Pionke, H.B. 1998. Reducing soil phosphorus solubility with coal combustion by-products. Journal of Environmental Quality 27, 111-118.

Teagasc 2008, Management data for Farm Planning 2008, Teagasc, Oak Park, Carlow.

Timoney, F. 2009. Codes of Good Practice for the use of biosolids in agriculture: Guidelines for farmers. Department of the Environment and Local Government and Agriculture: Available at http://www.environ.ie/en/Publications/Environment/Water/FileDownLoad,17228,en.pdf; accessed 12/1/10.

Captions for Tables

Table 1. Table showing cost of supply, delivery and addition of amendments, and increase in agitation costs and spreading costs due to increases in volumea and WEP of slurry 24 hr after application.

Table 2. Characterisation of PSMs used in the agitator test (mean ± standard deviation) tests carried out in triplicate, the maximum load of metals per hectare per treatment, maximum permissible annual average rates of addition of certain heavy metals to soils over a 10-yr period, background levels of these metals in mineral and organic soils, and limits on heavy metal concentrations in water drinking water extraction.

Table 1. Table showing cost of supply, delivery and addition of amendments, and increase in agitation costs and spreading costs due to increases in volumea and WEP of slurry at 24hr.

_________________________________________________________________________________________________________________________________

Chemicalb	Rate of addition		Cost c 		Rate		Spreading d	Agitation e	Cost waterf	Total	100 unit farm	P reduction	Metalsi	WEPj

€ / tonne	kg/m3		€/m3		€/m3		€/m3		€/m3	€/farm			% P 		kg/ha	mg/kg

None														1.6			0.50		0			2.1		1,240								2.64± 0.15

Alum			0.98:1 Al: P			150			23			1.6			0.51		0			5.6		3,310			83			49		0.51± 0.01

1.22:1 Al: P						29			1.6			0.51		0			6.5		3,840			94			61		0.27± 0.07

2.44:1 Al: P						58			1.6			0.53		0			10.9	6,470			99			122		0.03± 0.0

AlCl3 (PAC)		0.98:1 Al: P			280			18			1.6			0.51		0			7.2		4,300			87			49 		2.08± 0.06

1.22:1 Al: P						23			1.6			0.51		0			8.5		5,070			92			61		1.43± 0.02

2.44:1 Al: P						46			1.6			0.52		0			15		8,930			99			122		0.16± 0.02

FeCl2 (FeCl3)	2:1 Fe: P			250			14			1.6			0.51		0			5.7		3,370			88			100		2.43± 0.27

5:1 Fe: P						36			1.6			0.52		0			11.1	6,600			90			250		0.73± 0.06

10:1 Fe: P						72			1.7			0.54		0			20.2	11,100			99			500		0.4± 0 02

Ca(OH)2		1:1 Ca: P			312			2			1.6			0.50		0			2.6		1,570			0			50		1.7± 0.06

5:1 Ca: P						9			1.6			0.50		0			5		2,990			74			250		0.2± 0.02

10:1 Ca: P						19			1.6			0.51		0			8		4,760			81			500		0.05± 0.0

PSMs

Al-WTR-1		0.28 kg/kg			0			20			1.6			0.51		0			2.1		1,240			31					2.49± 0.06

(<2mm) g		0.69 kg/kg						50			1.9			0.61		0.3			2.8		1,670			77					1.73± 0.02

1.4 kg/kg						100			2.6			0.83		1.1			4.5		2,680			74					0.93± 0.02

Al-WTR-2		0.28 kg/kg			5			63			1.6			0.53		0.3			2.5		1,480			0					1.13± 0.05

(sludge) h		0.69 kg/kg						156			1.9			0.61		0.8			3.4		2,010			71					0.28± 0.01

1.4 kg/kg						313			2.5			0.81		1.6			5.5		3,270			67					0.07± 0.0

Flyash 			2.1 kg/kg			14			150			3.2			1.04		1.8			8.2		4,850			43					0.92± 0.14

4.2 kg/kg						300			4.9			1.58		3.6			14.3	8,480			72					0.21± 0.08

5.6 kg/kg						400			5.8			1.89		4.6			17.9	10,600			91					0.22± 0.04

FDGg			1.33 kg/kg			14			150			2.5			0.81		0.9			6.3		3,740			72					0.09± 0.0

2.65 kg/kg						300			3.6			1.17		2			11		6,520			89					0.05± 0.0

3.5 kg/kg						400			4.3			1.37		2.6			13.8	8,210			81					0.04± 0.0

______________________________________________________________________________________________________________________________________________________________________________________________________	______________

a These calculations are based a dairy farm with 100 cows, or equivalent stock, with a 18-wk winter. Sample slurry properties are based on based average values from this

study (TP = 811 mg/L, density of 1.01g/cm3 and dry matter content of 7.2%).

b  Ca(OH)2, AlCl3 (PAC) and FeCl2 (FeCl3) were laboratory chemicals; the most similar product on the market (in brackets) was chosen for cost estimates.

c Total cost of material, delivery of material and addition of material to slurry in slurry storage tank  per cubic meter of amendment used.

d Slurry spreading costs estimated based on data from Teagasc (S. Lawlor pers comm, 2010) and increase in volume of slurry due to amendment.

e Slurry agitating costs estimated based on data from Teagasc (2008)  with and increase in volume of slurry due to amendment.

f For ease of handling water DM must be approximately 10%. Some amendments resulted in DM >10%. Water would need to be added to the slurry to enable spreading.

g Al-WTR-1 <2 mm is alum-based water treatment residual which has been dried and crushed to pass the 2mm sieve

h Al-WTR-2 sludge is the homogenised alum-based water treatment residual in its natural state after water treatment and separation.

iTotal metal applied for each of the chemical amendments was calculated based on a slurry application rate of 50 m3/ha for each treatment.

j WEP of slurry 24 hr after start of agitator test.

Table	2.	Characterisation of PSMs used in the agitator test (mean ± standard deviation) tests carried out in triplicate, the maximum load of metals per hectare per treatment, maximum permissible annual average rates of addition of certain heavy metals to soils over a 10 year period and background levels of these metals in mineral and organic soils and limits on heavy metal concentrations in water drinking water extraction.

______________________________________________________________________________________________________

Parameter			By-product characterisation						Metal application ratea					Application	Background	d 			Water

Unit				Al-WTR-1	Al-WTR-2	Flyash		FGDb		Al-WTR-1	Al-WTR-2	Flyash	FGD	limits c		Mineral		Organic		limitse

(<2mm)		(Sludge)																				soil			soil																	kg/ha		kg/ha		kg/ha	kg/ha	kg/ha		kg/ha		kg/ha		mg/L

DM		%			100			32±	2		99.9± 0.01	37±	3

pH					7.9± 0.1		6.9± 0.2		11.2± 0.04	8.6± 0.01

WEP	mg/kg		<0.01					<0.01		<0.01

Al		%			11.1± 0.05	5.33± 1.2	5.66± 0.2	0.09± 0.0	280			420			848		6.75				97,000		70,000

As		mg/kg		6.2± 1.1		<0.01		13.3± 0.6 	 <0.01		0.02		0.02		0.2		0					31.5		26.7		0.05

Ca		%			1.3± 0.08	0.11± 0.0	4.85± 0.2	20± 0.3		32.4		8.6			730		1520				36,300		39,900

Cd		mg/kg		0.16± 0.03	<0.01		0.58± 0.03	0.17± 0.02	0.0004		0			0.009	0.0013	0.05		2.31		2.23		0.005

Co		mg/kg		0.49± 0.28	<0.01		33.3± 1.2	0.3± 0.14	0.0012		0			0.5		0.0025				21.7		16.7

Cr		mg/kg		3.8± 0.21	0.3± 0.02	88.3± 1.5	3± 0.1		0.01		0.0024		1.33	0.0225	3.5			126			74.9

Cu		mg/kg		31.7 ±1.5	0.63±0.03	32.7± 1.5	37± 13		0.08		0.005		0.49	0.28	7.5			64.5		57.5		0.05

Fe		%			0.24± 0.01	0.01±0.0	2.15± 0.1	0.06±0.01	6.1			0.8			320		4.5					52,300		49,800		0.3

K		%			0.03± 0.01	<0.01		0.1			0.03		0.67		0			15		2.25				26,600		18,600

Mg		mg/kg		165± 33		3.17± 1.7	12200± 	610	2950± 58	0.41		0.025		183		22.2				12,200		6,160

Mn		mg/kg		79± 1		6.87±0.1	347± 160	31± 0.6		0.2			0.05		5.2		0.325				2,780		2,050		0.05*

Mo		mg/kg		0.47± 0.2	<0.01		7.67± 0.5	0.73± 0.3	0.001		0			0.12	0.006				4.6			4.73

Na		mg/kg		611± 180	65± 14		1370± 610	660± 93		1.5			0.51		20.5	4.95				15,800		10,200

Ni		mg/kg		4.8± 0.06	0.6± 0.2		44± 1		11± 0.6		0.012		0.005		0.67	0.09	3			72.7		49.6

TP		mg/kg		234± 5.3	18.7± 1.6	5460± 630	65± 21		0.6			0.15		81.9	0.49				2,800		2,660		0.4*

Pb		mg/kg		1.2±0.8		<0.01		30± 1.7		0.74± 0.4	0.003		0			0.45	0.006	4			85.4		81.3		0.05

V		mg/kg		3± 0.2		0.2±0.01	155± 3.6	49± 2		0.008		0.0016		2.32	0.37				152			105

Zn		mg/kg		17± 0		0.8 ±0.1		75±	31		9.4 ±2		0.043		0.006		1.13	0.07	7.5			210			139			0.5*

_____________________________________________________________________________________________________________________

aThe maximum load of each metal per hectare for each treatment is tabulated based on a slurry application rate of 50m3/ha and the optimum rate for each amendment.

b FGD is flue gas desulphurisation product.

CGuideline limits in the Code of Good Practise for the use of biosolids in agriculture (Timoney, 2009) for the max permissible annual average rates of addition over a 10 year period.

dTotal metal and nutrient concentrations (95% percentile) of soil (Soil Geochemical Atlas of Ireland (Fay et al., 2010)) in upper 100mm of soil (bulk density 1.4 g/cm3).

eCharacteristics of surface water intended for the abstraction of drinking water (74/440/EEC), guidelines (*) where no mandatory limit.

Captions for figures.

Figure 1. Phosphorus released per unit surface area and DRP concentration in overlying water plotted against square root of time for undisturbed intact grassed sod only treatment () and grassed soil amended with slurry at a rate of 40 kg TP ha-1 (◊).

Figure 2. Total cost of chemical amendment of dairy cattle slurry including spreading and agitation costs plotted against the reduction in DRP lost to overlying water and the percentage reduction in DRP release to overlying water.

Figure 1.

| Mass of P released in the overlying water at time t (mg/m2) | 800 600 400 200 0 |  | 12 10 8 6 4 2 0 | Concentration of P in overlying water (mg/L) |
| --- | --- | --- | --- | --- |
|  |  | 0 1 2 3 4 5 |  |  |
|  |  | Square root of time after start of agitator (hours)0.5 |  |  |

Figure 2.

| Reduction in DRP loss from soil to overlying water (kg/ha) | 14 12 10 8 6 4 2 0 |  | 100 80 60 40 20 0 | Percentage reduction in DRP release to overlying water (%) |
| --- | --- | --- | --- | --- |
|  |  | 0 5 10 15 20 25 |  |  |
|  |  | Total cost of chemical amendment of dairy cattle slurry including spreading and agitation costs (€/tonne slurry) |  |  |

Note:

The amendments plotted (each at three rates) are ♦ aluminium sulphate, ● aluminium chloride, ▲ferric chloride, ■ burnt lime, ○Al-WTR, + flyash and ∆ FGD.